## Slide 1
SENSE · REAL ENVIRONMENT
Live water-condition inputs
TURBIDITY
TDS / SALINITY PROXY
PRESSURE / DEPTH
DS18B20 TEMPERATURE
ADC · 1-Wire · I²C
Environmental inputs provide the state used to select the next ping.
STM32F446RE · EMBEDDED CONTROL
Firmware in C / C++ on the payload's own MCU
THE NEXT PING IS COMPUTED FROM THE CURRENT ENVIRONMENT
STM32 NUCLEO-F446RE
Sensor interface boards
01
ACQUIRE
Read environmental inputs · reject stale / invalid readings
02
DECIDE
Smoothing + hysteresis → CLEAR / TRANSITION / MURKY
03
ADAPT
Centre / bandwidth · pulse duration · amplitude
04
SYNTHESISE
LFM · geometric · Barker-13 × Hann / Hamming / Blackman
05
STREAM
TIM6 + DMA → 12-bit DAC1 / PA4 · 1 MS/s
06
VERIFY
ADC + DMA capture → FFT · spectrogram · matched filter
ADAPTIVE NEXT PING
Parameters chosen per water condition
PARAMETER
CLEAR
TRANSITION
MURKY
CENTRE
42 kHz
40 kHz
38 kHz
BANDWIDTH
4 kHz
2 kHz
1 kHz
PULSE
2 ms
4 ms
8 ms
AMPLITUDE
35 %
50 %
62 %
CLEAR → shorter / sharper ping
MURKY → lower band / longer pulse / higher output demand
CONDITION · ANALOG FRONT END
LPF → TLV9062 → output
2nd-order low-pass · 70.7 kHz
op-amp gain ×1.5
AQUASDR PAYLOAD physical acrylic payload prototype for AUV integration
VALIDATION MCU ADC capture · FFT · spectrogram · matched filter
+ external instrument (oscilloscope / spectrum analyzer)
TECHNOLOGIES
TO BE USED
Embedded C/C++ · STM32F446RE · ADC · TIM6 · DMA · 12-bit DAC
Signal processing LFM · Geometric sweep · Barker-13 · FFT · Windowing
Analog Sallen-Key LPF · TLV9062
Software React · Node.js · Python · OpenSCAD
SENSE
DECIDE
ADAPT
SYNTHESISE
STREAM
CONDITION
VERIFY