## Slide 1: AquaSDR · TECHNICAL APPROACH
Your Team Name
Adaptive Software-Defined Sonar Transmitter for AUVs
SENSE
Real environment · real sensors
TDS / SALINITY PROXY
HC-SR04 · AIR RANGE
TURBIDITY
DS18B20 TEMPERATURE
PRESSURE / DEPTH
ADC · 1-Wire · I²C
Also on board BMP390 · IMU + magnetometer (I²C) · INA219 ×2 mounted, not commissioned
ONE POLICY · TWO INPUTS
A0 sensor
TDS_PROXY → ADC
Web command
console → UART
DECIDE · SYNTHESISE · STREAM
STM32F446RE embedded control · methodology & process
THE NEXT PING IS COMPUTED ON THE MCU
STM32 NUCLEO-F446RE
Sensor interface boards
MCU ADC CAPTURE
LFM example · on-board
Centre 42 kHz
Sweep 4 kHz
Pulse 2 ms Hann
330/330 cmds ACKed
0 DMA underruns
01
ACQUIRE
ADC · 1-Wire · I²C · stale / out-of-range inputs rejected
02
DECIDE
smoothing filter + hysteresis → CLEAR / TRANSITION / MURKY
03
SYNTHESISE
LFM · geometric sweep · Barker-13 × Hann / Hamming / Blackman
04
STREAM
TIM6 + DMA → 12-bit DAC1 / PA4 · 1 MS/s · 0 underruns
06
SELF-VALIDATE
ADC + DMA capture of the DAC output → FFT · spectrogram · matched filter
NEXT PING
Adaptive waveform parameters
CLEAR
TRANSITION
MURKY
CENTRE
42 kHz
40 kHz
38 kHz
BANDWIDTH
4 kHz
2 kHz
1 kHz
PULSE
2 ms
4 ms
8 ms
AMPLITUDE
35 %
50 %
62 %
Water condition changes → next-ping parameters change
05 CONDITION · ANALOG FRONT END
2nd-order low-pass filter
70.7 kHz design target
TLV9062 ×1.5
DESIGNED · NEXT BUILD
AQUASDR PAYLOAD · PHYSICAL PROTOTYPE acrylic payload hull
External scope validation → PENDING · AUV hull-slot pod → NEXT BUILD
TECHNOLOGIES
TO BE USED
Programming C / C++ · Python · JavaScript
Embedded STM32F446RE · ADC · TIM6 · DMA · 12-bit DAC
Signal processing LFM · geometric sweep · Barker-13 · FFT · windowing
Analog Sallen-Key LPF · TLV9062 op-amp
Software React · Node.js / Express · WebSocket · OpenSCAD
Hardware Turbidity · TDS · pressure · DS18B20 · IMU · BMP390 · INA219
SENSE
DECIDE
SYNTHESISE
STREAM
CONDITION
VERIFY
built / running
designed / next build