## Slide 1: AquaSDR · FEASIBILITY AND VIABILITY
Your Team Name
Proven on our hardware · risks identified · a mitigation for each
ANALYSIS OF FEASIBILITY
Readiness of every subsystem, from design to instrument validation
DESIGNED
SIMULATED
/ TESTED
BUILT
ON-BOARD
VERIFIED
INSTRUMENT
VALIDATED
Adaptive firmware engine
C/C++ on STM32F446RE
Timer + DMA + DAC streaming
TIM6 → DMA1 → DAC1 · 1 MS/s
LFM · geometric · Barker-13
with Hann / Hamming / Blackman
Sensor input + adaptation
CLEAR / TRANSITION / MURKY
Analog front end
Sallen-Key LPF + TLV9062
Payload enclosure
acrylic hull · printed AUV pod
n/a
n/a
Low-power operation
DMA-driven, CPU free per sample
n/a
reached
partly (A0 shown in CLEAR; printed pod next)
next
PROVEN ON THE BOARD · MCU ADC capture and firmware telemetry, not oscilloscope data
42.00 kHz
captured centre = calculated
LFM · Hann
−14.6 → −35 dB
spectral leakage, rect → Hann
window effect captured
−21.4 dB
Barker-13 sidelobe captured
−21.7 dB calculated
330 / 330
commands acknowledged
0 lost
0
DMA underruns
across every capture
< 100 ms
decision → new waveform
86–97 ms measured
CHALLENGES & RISKS → STRATEGIES
Each risk paired with how we overcome it
CHALLENGE
STRATEGY
STATUS
Frequency scale
PS cites 100–500 kHz; bench transducer is 40 kHz
Frequency-agnostic policy table; external high-speed DAC on the same TIM + DMA path
SCALE PATH
No oscilloscope on hand
external validation not yet possible
On-board ADC + DMA capture with FFT and matched filter now; lab scope at judging, CSV import ready
IN PLACE
Analog stage not yet built
filter + op-amp still to assemble
Two independent models agree within 0.02 dB in band; stock-value parts list ready
NEXT BUILD
Noisy or drifting sensor input
a bad reading could change the ping
Smoothing, hysteresis, stale and out-of-range rejection; TDS labelled as a proxy
IN PLACE
CPU load and battery budget
per-sample trig math is expensive
Next pulse computed between pings, DMA streams it; inline-meter power test planned
IN PLACE
Loss of control link
ping must never run unattended
Output off at boot, 2 s control lease auto-stop, DAC parked mid-scale on any fault
IN PLACE
Water ingress
payload must survive the hull slot
O-ring end caps; parametric pod compiled and fit-checked in OpenSCAD
DESIGNED
VIABILITY
Low-cost COTS
STM32 Nucleo · TLV9062 · standard passives
Software-defined
new waveform or policy = firmware update
Scalable
same architecture → 100–500 kHz with an external DAC
Maintainable
161 automated tests guard every change