## Slide 1
FEASIBLE TODAY
Already running on our STM32
payload, built from shelf parts
42.00 kHz
chirp lands exactly on target
−35 dB
leakage with Hann, from −14.6
< 100 ms
water change → new ping
0
DMA dropouts in every capture
CHALLENGES and how we beat them
01
RISK
Signal integrity
Stepped DAC output and sidelobes blur the echo
↓
STRATEGY
Hann / Hamming / Blackman windows + 70.7 kHz low-pass filter and op-amp stage
→ WINDOWS PROVEN · FILTER NEXT
02
RISK
Frequency & transducer
PS band is 100–500 kHz; our bench runs at 40 kHz
↓
STRATEGY
Same timer + DMA engine drives an external high-speed DAC and a matched driver stage
→ SCALE PATH READY
03
RISK
Bad sensor data
One noisy reading could flip the ping
↓
STRATEGY
Smoothing, hysteresis and out-of-range rejection before any change
✓ IN PLACE
04
RISK
Power & safety
Long missions drain the battery; a ping must never run away
↓
STRATEGY
DMA streams the pulse so the CPU stays free; 2 s auto-stop lease
✓ IN PLACE
VIABLE
Low cost
off-the-shelf STM32 + op-amp
Software-defined
new ping = firmware update
Scalable
same design → 100–500 kHz
Reliable
161 automated tests